Aether Engine

Register Table
Address	Name	R/W	Reset Value
0x0	Version	R		Indicates revision of the hardware
0x1	RamAddrLow	R/W	0x0000	Used ONLY when one of the tasks is writing data to the ram
0x2	RamAddrHigh	R/W	0x0000	The most significant bits where the contents in ram are stored
0x3	ConvConfig1	R/W	0x0401	The count of convolution engines used. Can go from 0 - 1024 (or max convolution engines installed). Also contains stride in upper msb, 0-63
0x4	ConvConfig2	R/W	0x0000	Accumulate enable, Write Results to Ram enable, then rest Matrix size
0x5	ConvConfig3	R/W	0x0000	Padding count 0-1024, extend (1) or zeros (0) the rest is for shifting of the data after accumulation
0x6	ConvConfig4	R/W	0x0000	Activation function 4 bits, activation function param is the rest
0x7	ConvStatus	R	0x0000	Convolution Done, Convolution Running, Current output count (truncated to fit, taking lsb)
0x8	Interrupt	R/W	0x0000	Interrupts signal when long running tasks finish. One interrupt pin. Each interrupt has and enable pin and is reset when the register is read
0x9
0xA
0xB
0xC
0xD
0xE	WriteToMem	W		Shift register to store a word. On write the data gets shifted
0xF	ReadFromMem	R		Shift register to read a word. On read data gets shifted

Instruction Table
Inst #	Name	Param 1 (4 bits)	Param 2 (16 bits)
0x0	NOP	X	XXXX	Does not do any more processing, but keeps processing what it was already doing
0x1	RST	Reset type: / 0: FULL / 1: CWGT (need?) / 2: CONV / 3: DWGT (need?) 4: DENS / default: FULL	XXXX	Reset different (or whole) parts chip. On layer change a reset might be needed, this is typically called throughout the code instead of only at the beginning.
0x2	RDR	Register #	XXXX	Reads the register at param 1 (Register #)
0x3	WRR	Register #	Data in #	Writes param 2 to param 1 register
0x4	LDW	1: CWGT / 2: DWGT / 3: STRT / 4: CONT / 5: MOVE / default: NOP	XXXX	Load weights from {Address upper reg, param 2} into either convolution or dense (for 1x1 convolution) / Invalid values do not do anything
0x5	CNV	Repeat Count # / 0: NOP	Address Lower #	Calculates the convolution, loading input data from {Address upper reg, param 2} until the whole matrix size (from reg) was pulled, it then repeats repeat count # times.
0x6	DNS	Repeat Count # / 0: NOP	Address Lower #	Does the dense layer / Dense Mode on Config Reg: / loading in activation then weights, repeating for every dense element. / 1x1 conv mode on Config Reg: / Load in activation and not weights
0x7	LIP	Load Location / 1: STRT / 2: CONT / default: NOP	Data in #	Load Input data
0x8	ROP	Read Type / 1: STRT / 2: CONT / default: NOP	XXXX	Read data output
0x9
0xA
0xB
0xC
0xD
0xE
0xF

0x0 - VERSN:
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
RST	0	1	1	0	1	1	0	0	0	0	0	0	0	0	0	0
R/W	Read Only
Content	Chip ID								Major Version					Minor

Version Register

0x1 – HWRID:
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
RST	1	0	1	1	0	0	1	0	1	1	1	0	1	0	0	1
R/W	Read Only
Content	Unique Number Based on Set Configuration

Hardware ID Register

0x2 – MEMUP:
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
RST	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0
R/W	Read / Write
Content	StartMemAddr[31:16] and EndMemAddr[31:16]

Memory Upper Register
0x3 – MSTRT:
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
RST	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0
R/W	Read / Write
Content	StartMemAddr[15:0]

Start Memory Address Register

0x4 – MENDD:
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
RST	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0
R/W	Read / Write
Content	EndMemAddr[15:0]

End Memory Address Register

0x5 – BCFG1:
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
RST	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	1
R/W	Read / Write
Content	Shift [3:0]				Engine Count

Base Config 1 Register
Shift: 63 bits maximum, is split between base config1 and 2. This is the shift when executing the mac operation
Engine Count: 0 – 4096

0x6 – BCFG2:
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
RST	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0
R/W	Read / Write
Content	Shift [5:4]		Matrix Size

Base Config 2 Register
Matrix Size: the size of the matrix with any padding, used to do correct number of cycles

0x7 – BCFG3:
	15	14	13	12	11	10	9	8		7		6		5		4		3		2		1		0
RST	0	0	0	0	0	0	0	0		0		0		0		0		0		0		0		0
R/W	Read / Write
Content	LD FRM		ShiftFinal

Base Config 3 Register
LD FRM: Load From,
0: input data buffer
1: ram (at address specified later)
2: convolution output (engine count will be based on memory value)
ShiftFinal: Shifts from the output of mac (2N+1) so it can fit in the (N) sized register

0x8 – CPRM1:
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
RST	0	0	0	0	0	0	0	0	0	1	0	0	0	0	0	0
R/W	Read / Write
Content	Padding			Pfil	Stride						Activ FN			Accu	SVR	SVB

Conv Run Param 1 Register
Padding: up to 7 spaces on each side, same vertical and horizontal
Pfil: fills with 0 when 0 and fills with closes pixel (or value) when 1

Activ FN: activation function. (only applied on data output and when AFN is set)
0: None
1: Relu
2: tbd
3: tbd
4: tbd
default: None
Accu – Accumulate values (1: yes, 0: no)
SVR – Save values to ram
SVB – Save values to buffer
AFN – Apply the activation function on export

0x9 – STATS:
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
RST	0	0	1	0	0	0	1	0	0	1	0	0	0	0	0	0
R/W					Read / Write					Read Only
Content					Een	Cen	Den	Men		Crn	Drn	Mrn	Eac	Cac	Dac	Mac

Device Status Register and Interrupt
Een – Error Interrupt enabled
Cen – Convolution Interrupt enabled
Den – Dense Interrupt enabled
Men- Memory Interrupt enabled

Crn – Convolution Running
Drn – Dense Running
Mrn – Memory Task Running

When the corresponding en signal is set these are cleared on stat reg read instruction, when not set these signals will clear themselves when they normally would
Eac – Error Asserted
Cac – Convolution Done
Dac – Dense Done
Mac – Memory Task Done

0xA - Register:
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
RST	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0
R/W
Content											Error Code

0xB - Register:
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
RST	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0
R/W
Content

0xC - Register:
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
RST	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0
R/W
Content

0xD - Register:
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
RST	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0
R/W
Content

0xE - Register:
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
RST	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0
R/W
Content

0xF - Register:
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
RST	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0
R/W
Content