Aether Engine

Register Table
Address	Name	R/W	Reset Value
0x0	Version	R		Indicates revision of the hardware
0x1	RamAddrLow	R/W	0x0000	Used ONLY when one of the tasks is writing data to the ram
0x2	RamAddrHigh	R/W	0x0000	The most significant bits where the contents in ram are stored
0x3	ConvConfig1	R/W	0x0401	The count of convolution engines used. Can go from 0 - 1024 (or max convolution engines installed). Also contains stride in upper msb, 0-63
0x4	ConvConfig2	R/W	0x0000	Accumulate enable, Write Results to Ram enable, then rest Matrix size
0x5	ConvConfig3	R/W	0x0000	Padding count 0-1024, extend (1) or zeros (0) the rest is for shifting of the data after accumulation
0x6	ConvConfig4	R/W	0x0000	Activation function 4 bits, activation function param is the rest
0x7	ConvStatus	R	0x0000	Convolution Done, Convolution Running, Current output count (truncated to fit, taking lsb)
0x8	Interrupt	R/W	0x0000	Interrupts signal when long running tasks finish. One interrupt pin. Each interrupt has and enable pin and is reset when the register is read
0x9
0xA
0xB
0xC
0xD
0xE	WriteToMem	W		Shift register to store a word. On write the data gets shifted
0xF	ReadFromMem	R		Shift register to read a word. On read data gets shifted

Name	Short Name	Description
Reset	rst 0xXXXXX	Ability to reset certain modules or the whole chip
No Operation	nop 0x00000	Continues processing long running commands but does not start anything else
Write Reg	wrl 0xADDDD	Writes 0xDDDD to the register 0xA
Read Reg	rrl 0xAXXXX	Reads 0xDDDD on output from the register 0xA
Load Weights	lcw 0xMXXXX	Loads weights of M task starting at ram address {RamMsb, 0xXXXX}
Start Task	sc 0xMXXX	Starts the M task with layer data starting at ram address {RamMsb, 0xXXXX}