Aether Engine

Register Table
Address	Name	R/W	Reset Value
0x0	Version	R		Indicates revision of the hardware
0x1	RamAddrLow	R/W	0x0000	Used ONLY when one of the tasks is writing data to the ram
0x2	RamAddrHigh	R/W	0x0000	The most significant bits where the contents in ram are stored
0x3	ConvConfig1	R/W	0x0401	The count of convolution engines used. Can go from 0 - 1024 (or max convolution engines installed). Also contains stride in upper msb, 0-63
0x4	ConvConfig2	R/W	0x0000	Accumulate enable, Write Results to Ram enable, then rest Matrix size
0x5	ConvConfig3	R/W	0x0000	Padding count 0-1024, extend (1) or zeros (0) the rest is for shifting of the data after accumulation
0x6	ConvConfig4	R/W	0x0000	Activation function 4 bits, activation function param is the rest
0x7	ConvStatus	R	0x0000	Convolution Done, Convolution Running, Current output count (truncated to fit, taking lsb)
0x8	Interrupt	R/W	0x0000	Interrupts signal when long running tasks finish. One interrupt pin. Each interrupt has and enable pin and is reset when the register is read
0x9
0xA
0xB
0xC
0xD
0xE	WriteToMem	W		Shift register to store a word. On write the data gets shifted
0xF	ReadFromMem	R		Shift register to read a word. On read data gets shifted

Instruction Table
Inst #	Name	Param 1 (4 bits)	Param 2 (16 bits)
0x0	NOP	X	XXXX	Does not do any more processing, but keeps processing what it was already doing
0x1	RST	Reset type: / 0: FULL / 1: CWGT (need?) / 2: CONV / 3: DWGT (need?) 4: DENS / default: FULL	XXXX	Reset different (or whole) parts chip. On layer change a reset might be needed, this is typically called throughout the code instead of only at the beginning.
0x2	RDR	Register #	XXXX	Reads the register at param 1 (Register #)
0x3	WRR	Register #	Data in #	Writes param 2 to param 1 register
0x4	LDW	1: CWGT / 2: DWGT / default: NOP	Address Lower #	Load weights from {Address upper reg, param 2} into either convolution or dense (for 1x1 convolution) / Invalid values do not do anything
0x5	CNV	Repeat Count # / 0: NOP	Address Lower #	Calculates the convolution, loading input data from {Address upper reg, param 2} until the whole matrix size (from reg) was pulled, it then repeats repeat count # times.
0x6	DNS	Repeat Count # / 0: NOP	Address Lower #	Does the dense layer / Dense Mode on Config Reg: / loading in activation then weights, repeating for every dense element. / 1x1 conv mode on Config Reg: / Load in activation and not weights
0x7	LIP	Load Location / 0: STRT / 1: CONT	Data in #	Load Input data
0x8	ROP	Read Type / 0: STRT / 1: CONT	XXXX	Read data output
0x9
0xA
0xB
0xC
0xD
0xE
0xF

0x0 - Version Register:
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
RST	0	1	1	0	1	1	0	0	0	0	0	0	0	0	0	0
R/W	Read Only
Content	Chip ID								Major Version					Minor

0x1 - RamAddrLow Register:
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
RST	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0
R/W	Read / Write
Content	Ram Low Address

0x2 - RamAddrHigh Register:
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
RST	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0
R/W	Read / Write
Content	Ram High Address

0x3 - ConvConfig1 Register:
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
RST	0	0	0	0	0	1	0	0	0	0	0	0	0	0	0	1
R/W	Read / Write
Content	Stride				Engine Count

0x4 - ConvConfig2 Register:
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
RST	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0
R/W	Read / Write
Content	Accu	SVR	Matrix Size

0x5 - ConvConfig3 Register:
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
RST	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0
R/W	Read / Write
Content	Padding									Pfil	Shift Amount

0x6 - ConvConfig4 Register:
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
RST	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0
R/W	Read / Write
Content	Activation Function				Activation Params

0x7 - ConvStatus Register:
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
RST	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0
R/W	Read Only
Content	Done	RNG	Count

0x8 - Interrupt Register:
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
RST	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0
R/W	R/W	R	R/W	R	R/W	R
Content	Men	Mac	Cen	Cac	Den	Dac

0x9 - Register:
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
RST	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0
R/W
Content

0xA - Register:
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
RST	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0
R/W
Content

0xB - Register:
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
RST	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0
R/W
Content

0xC - Register:
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
RST	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0
R/W
Content

0xD - Register:
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
RST	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0
R/W
Content

0xE - WriteToMem Register:
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
RST	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0
R/W	Write Only
Content	Memory Bits

0xF - ReadFromMem Register:
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
RST	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0
R/W	Read only
Content	Memory Bits